Signals, Encoding and Modulation
Gihan Dias
CS2032 – Principles of Computer Communication
with slides by Sulochana Sooriyaarachchi
2017 Batch – Jan 2019

---
Outcomes
After successful completion of this lesson you will be able t0:
Identify and compare different techniques for encoding data into signals

---
Encoding and Modulation
- Encoding takes a digital or an analog signal and converts it to a form suitable for sending on a wire or a fibre
  - Baseband
- Modulation takes a digital or an analog signal and modifies a carrier signal with it
  - Passband (also called Broadband)

---
Encoding and Modulation

---
Forms of Encoding and Modulation
Digital Data, Digital Baseband Signal
  - e.g. Computer file sent on a Network cable
Digital Data, Analog Carrier (broadband) Signal
  - e.g. a computer file sent on a wireless network
- Analog Data, Digital Data
  - e.g. sound stored on computer
  - can then be transmitted on a baseband or carrier signal
- Analog Data, Analog Carrier Signal
  - e.g. sound transmitted on FM radio

---
Digital Data,
Digital Baseband Signal
Data bits encoded into voltage pulses

---
NRZ
NoReturn to Zero-Level (NRZ-L)
Presence (0) or absence (1) ofvoltage
NoReturn to Zero, Invert on ones (NRZI)
Presence (1) or absence (0) of a transition
A differential encoding

---
Multilevel Binary
Uses more than 2 signal levels
Bipolar AMI
No signal (0), positive pulse (1) and negative pulse (1)
Pseudoternary
No signal (1), positive pulse (0) and negative pulse (0)

---
Biphase
Transition at the middle of bit period as clocking
Manchester
Midbittransition for both clocking and data
Low-to-high (1), high-to-low (0)
Differential Manchester
Midbittransition only for clocking
Transition at beginning of bit period(0), no transition at the beginning of bit period(1)

---
Scrambling schemes

---
Scrambling schemes(2)
Bipolar with8-ZerosSubstitution (B8ZS)
Replace octets of all zeros with000+-0-+if the last pulse preceding the octet is positive
Replace octets of all zeros with000-+0+-if the last pulse preceding the octet is negative
High-DensityBipolar3-zeros (HDB3)
Replace strings of 4 zeros
	Number of Bipolar Pulses (ones) since Last Substitution
Polarity of preceding pulse	odd	even
-	000-	+00+
+	000+	-00-

---
Desired Characteristics of Signal
No dc component
As many transitions as possible for synchronization
Noticeable difference in signal levels
Manageable range of frequency components to reconstruct the signal after transmission

---
Comparison
NRZ-L: difficult to synchronize sender and receiver
E.g. bit string of all ones or all zeros
NRZ-I: synchronization still is problematic
E.g. bit string of all zeros
NRZ is simple and low cost to implement
Multilevel Binary: cancels off dc component as much as possible by alternating sign of voltage levels
Manchester and Differential Manchester: clocking information is embedded in the signal itself

---
Digital Data, Analog Signal
1. e.g. 1) To produce analog signal of voice frequency range, to transmit over telephone network
2. 2) to transmit digital data on an radio freq. carrier
3. Operates on one or more of
- Amplitude,
- Frequency and
- Phase
of the carrier signal

---
Amplitude Shift Keying (ASK)
Two amplitudes to represent two binary values
Multiple amplitudes for representing multiple bits

---
Frequency Shift Keying (FSK)
Two frequencies to represent two binary values (BFSK)
Multiple frequencies to represent multiple bits at a time (MFSK)

---
Phase Shift Keying (PSK)
Two phases to represent two binary values (BPSK)
Multiple phases to represent multiple bits

---
Analysis of A/F/PSK
One amplitude/frequency/phase per single bit gives a data rate equals to baud rate
Higher data rates
Representing multiple bits with a single amplitude/frequency/phase
n bits per amplitude/frequency/phase assign 2^n amplitudes/frequencies/phases for combinations
More different signals  More bits per baud
Combine amplitude, frequency and phase shifts
Signals are represented in constellation diagram

---
Constellation Diagram
Q-axis
Amplitude (A) and phase shifts (α) of a given sinusoidal signal is plotted with dots
Each dot interprets a bit string
I: In-phase axis, Q:Quadratureaxis
1011
A
α
I-axis

---
QuadratureAmplitude Modulation
(QAM)
Combination of Amplitude and Phase Shifts
E.g. a set of signals is given in Figure 1
I-axis
Q-axis
5
000
3
110
101
100
011
010
001
111
Figure 1: constellation diagram

---
Analog Data,
Digital Data
The Digital Data may then be transmitted on a baseband or carrier signal

---
Introduction
Converting analog data to digital data (digitization)
Codec:converts analog data into digital form and recovers the original analog data from digital signal
Techniques used in codec
Pulse Code Modulation (PCM)
Delta Modulation (DM)

---
PCM – How to
Divide the amplitude range into levels
Assign each amplitude level a bit pattern ofnbits
Sample the analog signal periodically
Approximate the amplitude of each sample to the most closely matching level
111
.
.
.
001
000

---
Analysis of PCM
Accuracy of reconstructed signal
Sampling rate?
Number of amplitude levels?

---
Delta Modulation (DM)
analog input is approximated by a staircase function
can move up or down one level ( ) at each sample interval
has binary behavior
since function only moves up or down at each sample interval
can encode each sample as single bit (1 for up or 0 for down)

---
DM …continued

---
Analog Data, Analog Signal
Modulating signal
Modulated signal

---
Introduction
Moving a signal from its baseband to a different frequency band (Modulation)
Data is modulated on to a carrier wave
Principal techniques:
Amplitude Modulation (AM)
Angle Modulation
Frequency Modulation (FM)
Phase Modulation (PM)

---
Amplitude Modulation (AM)
where A(t) is the amplitude of the modulated signal, is the amplitude of the carrier signal is the modulation index
Modulator
Carrier component
Side bands
Acknowledgement: Prof. Dileeka Dias

---
Example
Carrier signal
Modulated signal
Modulating signal

---
Angle Modulation
Modulated Signal
For Phase Modulation
For Frequency Modulation
Modulation index is the change of modulated variable with respect to the modulating signal
Acknowledgement: Prof. Dileeka Dias

---
Frequency Modulation (FM)
Carrier
Modulating signal
Modulated signal

---
Phase Modulation (PM)
Carrier
Modulating signal
Modulated signal

---
Thank you