Transmission II
Gihan Dias
Sulochana Sooriarachchi
CS2032 – Principles of Computer Communication

---
Transmission Errors
“I heard from your brother in Finland. Plan to meet there tomorrow”
TRANSMISSION ERROR
“I heard from your brothel in Finland. Plan to meet there tomorrow”

---
Introduction
Introduction
- Error: an alteration of one or more bits between transmission and reception
- Error Detection: know that an error has occurred
  - Discard the message, notify the sender, sender retransmits
  - Receiver corrects the error (Error Correction) and uses the message
Types of errors:
  - Single bit errors – only one bit has changed
  - Error bursts – two or more bits, the first and last of which are in error

---
Error Detection Techniques:
Sending additional bits, value of which depends on the data
E.g. Parity check, Cyclic Redundancy Check (CRC)

---
Parity Check
Parity Check
- Count 1-bits in the data
- Parity bit:
  - Odd parity => add a bit such that the total number of 1’s in the block of data becomes odd
  - Even parity => add a bit such that the total number of 1’s in the block of data becomes even
  This added bit is called the Parity Bit

---
Parity – Pros and Cons
Parity – Pros and Cons
- Can detect single bit errors
- E.g. A bit stream transmitted at a speed of 19.2 Kbps was interrupted by an electrical surge lasted for 0.01 sec. How many bits may get affected?
  - Single bit errors are unlikely
E.g. A block of bits sent over parallel cable and a single path get damaged
  - Single bit errors!
Parity is the basis for more sophisticated error detection techniques

---
Parity
Parity
For double bit error detection
  - Two parity bits; one for odd numbered bits (bit 1, 3, 5, 7…) and the other for even numbered bits (bit 2, 4, 6, 8…)
Burst Error Detection
  - Sending data bits in separate frames with each frame having a parity bit on its own: e.g. Data block sent as a two dimensional array

---
Cyclic Redundancy Check (CRC)
Cyclic Redundancy Check (CRC)
- Based on Polynomial Division
- Bit strings are interpreted as polynomials
- Sender and receiver agree upon a Generator Polynomial

---
Steps
Steps
Generator Polynomial
1. Append number of zeros to the bit string, the number that is equal to the order of
2. Get the polynomial for the resulting bit string in (1)
3. Divide by and get the remainder
4. Get where
5. Send
6. Say is what the receiver gets
7. Receiver must divide by
  - If remainder is 0 then the message is correctly received

---
Modulo 2 Arithmetic
Modulo 2 Arithmetic
Modulo 2 Division e.g.
Modulo 2 Additions
  0 + 0 = 0
  1 + 0 = 1
  0 + 1 = 1
  1 + 1 = 0
Modulo Subtraction
  0 – 0 = 0
  1 – 0 = 1
  0 – 1 = 1
  1 – 1 = 0
				1	0	0	0	1	1	1
1	1	0	0	1	1	1	0	0	0	0	0	1	0	1	0
				1	1	0	0	1
				0	0	0	1	0
				0	0	0	0	0
				0	0	1	0	0
				0	0	0	0	0
				0	1	0	0	1
				0	0	0	0	0
				1	0	0	1	0
				1	1	0	0	1
				1	0	1	1	1
				1	1	0	0	1
				1	1	1	0	0
				1	1	0	0	1
				0	1	0	1

---
Example!!!!
Example!!!!
- Send the Bit String 1101011
- Generator Polynomial is

---
CRC Implementation
CRC Implementation
Using Circular Shifts
  - Needs only to Shift and XOR
Steps
1. Interpret as
2. Shift register has r bits: rightmost position corresponds to and leftmost bit if for
3. An XOR circuit lies to the right of any position for which the corresponding is 1. The leftmost bit position of the register is feed as one of the operands to XOR
4. Initialize the register to all Zeros
5. Input the bit string as one bit at a time from rightmost bit position of the register

---
Example!!!!
- Implement the Circular Shifting circuit for Generator Polynomial
- Send the Bit String 1010001101
	Cr	Cr-1	…	C0
initial	0	0		0
Step 1
Step 2
. / . / .
Step n

---
Error Correction
Detect, locate and correct erroneous bits

---
Hamming Code
Hamming Code
Hamming distance
  - E.g. v1 = 011011, v2=110001
  - The number of bits in which v1 and v2 do not agree is called the Hamming distance.
  - Then d(v1, v2) = 3
Block code technique:
  - Map k-bit sequences into n-bit codewords
  - Invalid codeword correspond to minimum hamming distance

---
Block Code Example!!
Block Code Example!!

---
Thank you