Transmission Media
Gihan Dias
Sulochana Sooriarachchi
CS2032 – Principles of Computer Communication

---
Lesson Outcomes
Lesson Outcomes
After successful completion of this lesson you will be able to:
  - Categorize different technologies of transmission media
  - Explain concepts behind the functioning of media

---
Types of Transmission Media

---
Characteristics of Media
Characteristics of Media
- Cost
- Data Rate
- Bandwidth
  - higher bandwidth gives higher data rate
transmission impairments
  - eg. attenuation
Interference
  - Causes: electric motors, lightning strikes, other wires, spark
number of receivers in guided media
  - more receivers introduces more attenuation

---
Guided Media

---
Twisted Pair
Twisted Pair
Copper
  - Conductive
  - Resistance to corrosion
Twist
  - Straight copper act as antennas and pick extraneous signals
  - Insulated copper wires are twisted
  - Twist reduces signal interference between pairs (Crosstalk)
Distance causes signals to lose strength (Attenuation)

---
Coaxial Cable
Coaxial Cable
Metallic shield is a wire mesh
  - Protect signals from electromagnetic interference
Can transmit in
  - Baseband mode: bandwidth devoted for single stream of data
  - Broadband mode: multiple signals over multiple channels

---
Unshielded vs Shielded TP
Unshielded vs Shielded TP
unshielded Twisted Pair (UTP)
  - ordinary telephone wire
  - cheapest
  - easiest to install
  - suffers from external EM interference
shielded Twisted Pair (STP)
  - metal braid or sheathing that reduces interference
  - more expensive
  - harder to handle (thick, heavy)
in a variety of categories - see EIA-568
Dept. of Computer Science & Engineering, 2008

---
Optical Fiber
Optical Fiber
- Light waves in place of electricity
- Long distance transmission
  - Impervious to electrical noise
  - Large capacity
  - Very thin, therefore can bundle large numbers in manageable sized cables

---
Basics of  Optical Fiber
Basics of
Optical Fiber
Refraction
  - if medium 2 has higher optical density
  - if medium 1 has higher optical density
Index of refraction
  - Index < 1 : light travel to less optically dense medium
  - Index>1: light travel to more optically dense medium
When α is less than a critical angle, there is no refracted light
β>α
α>β
α
β
α
Interface between two media
Light Source
Reflected Light
Refracted Light
2
1

---
Basics of Optical Fiber…(2)
Basics of Optical Fiber…(2)
Light source
  - LED or Laser
  - Short rapid light pulses at different angles
- Light bounces boundary to boundary and propagate
- Detected by a sensor at the receiver
- Finite number of angles possible
  - Each angle defines a path or mode
  - Step Index Multimode Fiber

---
Basics of Fiber (3)
Basics of Fiber (3)
Modal Dispersion: larger the angle of reflection faster it reaches destination and vice versa
  - Light from one pulse catch light from other and viewed by sensor as a steady stream of light  loss of coded data
Graded Index Multimode Fiber:
  - Reduce modal dispersion by making material become gradually less dense when moving out radially from core
Single Mode Fiber:
  - Reduce core diameter until single angle of light is possible

---
Advantages of Optical Fiber
Advantages of Optical Fiber
- Can transmit more data than conductive metal
- Less resistance to light, can travel far without repeaters
- Not affected by electro magnetic interference
- High resistance to environmental elements like humidity
However, a level of complexity is added because of the need for conversion from light to electrical signals and vice versa

---
Wireless
No physical connection

---
Basics
Basics
- Oscillating electromagnetic waves of a transmitting antenna
- Travels through air (free space)
- Sensed by receiving antenna

---
Electromagnetic Wave Spectrum
Electromagnetic Wave Spectrum

---
Wireless Transmission Frequencies
Wireless Transmission Frequencies
2GHz to 40GHz
  - microwave
  - highly directional
  - point to point
  - satellite
30MHz to 1GHz
  - omnidirectional
  - broadcast radio
3 x 1011 to 2 x 1014
  - infrared
  - local
Dept. of Computer Science & Engineering, 2008

---
Antennas
Antennas
- electrical conductor used to radiate or collect electromagnetic energy
- transmission antenna
  - radio frequency energy from transmitter
  - converted to electromagnetic energy by antenna
  - radiated into surrounding environment
reception antenna
  - electromagnetic energy impinging on antenna
  - converted to radio frequency electrical energy
  - fed to receiver
same antenna is often used for both purposes
Dept. of Computer Science & Engineering, 2008

---
Radiation Pattern
Radiation Pattern
- power radiated in all directions
- not same performance in all directions
  - as seen in a radiation pattern diagram
an isotropic antenna is a (theoretical) point in space
  - radiates in all directions equally
  - with a spherical radiation pattern
Dept. of Computer Science & Engineering, 2008

---
Parabolic Reflective Antenna
Parabolic Reflective Antenna
Dept. of Computer Science & Engineering, 2008

---
Antenna Gain
Antenna Gain
- measure of directionality of antenna
- power output in particular direction verses that produced by an isotropic antenna
- measured in decibels (dB)
- results in loss in power in another direction
- effective area relates to size and shape
  - related to gain
Dept. of Computer Science & Engineering, 2008

---
Terrestrial Microwave
Terrestrial Microwave
- used for long haul telecommunications
- and short point-to-point links
- requires fewer repeaters but line of sight
- use a parabolic dish to focus a narrow beam onto a receiver antenna
- 1-40GHz frequencies
- higher frequencies give higher data rates
- main source of loss is attenuation
  - distance, rainfall
also interference
Dept. of Computer Science & Engineering, 2008

---
Satellite Microwave
Satellite Microwave
- satellite is relay station
- receives on one frequency, amplifies or repeats signal and transmits on another frequency
  - eg. uplink 5.925-6.425 GHz & downlink 3.7-4.2 GHz
typically requires geo-stationary orbit
  - height of 35,784km
  - spaced at least 3-4° apart
typical uses
  - television
  - long distance telephone
  - private business networks
  - global positioning
Dept. of Computer Science & Engineering, 2008

---
Satellite Communication Configuration
Satellite Communication Configuration

---
Broadcast Radio
Broadcast Radio
- radio is 3kHz to 300GHz
- use broadcast radio, 30MHz - 1GHz, for:
  - FM radio
  - UHF and VHF television
- is omnidirectional
- still need line of sight
- suffers from multipath interference
  - reflections from land, water, other objects
Dept. of Computer Science & Engineering, 2008

---
Infrared
Infrared
- modulate non-coherent infrared light
- end line of sight (or reflection)
- are blocked by walls
- no licenses required
- typical uses
  - TV remote control
  - IRD port
Dept. of Computer Science & Engineering, 2008

---
Wireless Propagation Ground Wave
Wireless Propagation
Ground Wave
Waves follow earth’s curvature and propagate despite obstacles due to;
  - Currents induced by waves on the earth’s surface cause the wavefront to slow down tilt downward
  - Diffraction at obstacles

---
Wireless Propagation Sky Wave
Wireless Propagation
Sky Wave
Refraction causes waves to bounce back and forth between earth’s surface and the ionosphere (ionizes layer of upper atmosphere)

---
Wireless Propagation Line of Sight
Wireless Propagation
Line of Sight
Neither refraction no ground wave propagation works for high frequency waves above 30MHz
  - Need Satallites
At ground level antennas must be places at effective line of sight
  - “effective” distance depends on bent of waves with earth curvature and refraction by atmosphere

---
Line of Sight Transmission
Line of Sight Transmission
Free space loss
  - loss of signal with distance
Atmospheric Absorption
  - from water vapour and oxygen absorption
Multipath
  - multiple interfering signals from reflections
Refraction
  - bending signal away from receiver
Dept. of Computer Science & Engineering, 2008

---
Transmission Impairments
Common to both guided and unguided media

---
Free Space Loss
Free Space Loss
- Attenuation due to spread of the signal over large area
- Expressed by ratio of Radiated Power to Received Power

---
Multipath Interference
Multipath Interference
- Signal is reflected by obstacles and multiple copies of the signal reaches the receiver with varying delays
- In microwave, signal may refract and also go through curve paths so that it will reflect from ground
Dept. of Computer Science & Engineering, 2008

---
Transmission Media Standards

---
Standards
Standards
- V-Series: for telephone communication
- X Series: for interfaces
(by CCITT – Comete` Consultatif Internationale de Te`le`graphique at Te`le`phonique = International Consultative Committee for Telephony and Telegraphy)
- EIA – electrical connections and physical transfer of data between devices
- IEEE – LAN, WAN, Wireless..
  - We will cover IEEE 802 Wired and Wireless Communication

---
Thank You